Greenhouse CO₂ Controller Documentation
1. Introduction
The goal of this project is to design and implement a CO₂ fertilization controller system for a greenhouse. The controller maintains the CO₂ concentration at a level defined by the user through a local interface. The maximum configurable CO₂ setpoint is 1500 ppm. For safety reasons, if the CO₂ concentration exceeds 2000 ppm at any time, the ventilation system is automatically activated to reduce the level.
The controller also supports persistence of user settings using EEPROM memory, ensuring that configurations are retained after power cycles. Additionally, the system communicates with a cloud service (ThingSpeak) to send environmental measurements and receive remote commands, thus enabling monitoring and control from outside the greenhouse.
2. System Overview
The greenhouse CO₂ controller integrates sensing, control, actuation, and cloud connectivity:
- Sensors measure CO₂ concentration, relative humidity, temperature, and pressure.
- Controller (based on Raspberry Pi Pico W) processes sensor inputs, applies control logic, and manages data storage and communication.
- Actuators regulate the greenhouse environment: ventilation fan speed and CO₂ injection valve.
- User interface allows local configuration of CO₂ setpoints and visualization of sensor data.
- Cloud connection (ThingSpeak) provides remote monitoring and command reception.
The data flow can be summarized as:
Sensors → Pico controller → Control decisions → Actuators + Cloud reporting.
3. Hardware
Controller Platform
- Raspberry Pi Pico W with RS-485 interface for Modbus communication.
- EEPROM for persistent storage of parameters.
Sensors
1. Vaisala GMP252 (CO₂ probe)
  1. Modbus address: 240
  2. Provides greenhouse CO₂ concentration measurement.
2. Vaisala HMP60 (Temperature and Relative Humidity sensor)
  1. Modbus address: 241
  2. Provides temperature (°C) and relative humidity (%) values.
3. Sensirion SDP610 (Differential Pressure sensor)
  1. Interface: I²C bus
  2. Address: 0x40
  3. Connected via SCL (Pin 15) and SDA (Pin 14)
  4. Measures pressure difference between greenhouse and ventilation duct
  5. Provides signed 16-bit values requiring conversion into physical units (Pa).
Actuators
- Produal MIO 12-V module (Modbus address 1)
  - Analog Output (0–10 V) controls the ventilation fan speed.
  - Digital counter input monitors fan rotation pulses to verify operation.
- CO₂ injection valve connected to GPIO27
  - Controls release of CO₂ at a rate of ~17 l/min.
  - Requires careful timing to prevent rapid concentration spikes.
Additional Components
- OLED display and rotary encoder for local UI.
- Wi-Fi connectivity through Pico W.

4. Software
- Task structure (UI task, controller task, network task, etc.)
- Sensor and actuator management
- EEPROM storage of settings
- Safety handling (CO₂ >2000 ppm ventilation override)
- Pico simulator functionalities and limitations
5. User Interface (UI)
- Hardware (OLED display, rotary encoder, buttons)
- Setting the CO₂ setpoint
- Display of measurements (CO₂, humidity, temperature, pressure, fan speed)
- Persistence of settings

6. Cloud Connection (ThingSpeak)
The system integrates with the ThingSpeak cloud platform using a RESTful API. The Pico controller periodically transmits environmental data and control parameters to the cloud. The API also allows reception of remote commands, such as setpoint adjustments.
Data Sent to Cloud
1. CO₂ level (ppm)
2. Relative humidity (%)
3. Temperature (°C)
4. Ventilation fan speed (0–100%)
5. CO₂ setpoint (ppm)
Data Format
- Sent as HTTP POST requests.
- Fields follow the format: fieldX=value where X corresponds to the measurement ID.
- Example: field1=450 indicates a CO₂ concentration of 450 ppm.
- Multiple fields are included in a single request.
Additional metadata such as timestamps or system status may be included.
Security and Configuration
- Network credentials and ThingSpeak API keys are stored in EEPROM.
- Parameters can be configured via the local UI.
7. Test Systems
Full-Scale Test System
- Includes the actual hardware setup with real sensors and actuators.
- Ventilation fan connected through Produal MIO 12-V.
- Provides realistic CO₂ distribution and environmental dynamics.
Miniature Test System
- Replicates the architecture but with smaller, partially simulated components.
- Some sensors are simulated using a second Pico device.
- Differences:
  - Smaller fan, lower pressure differences.
  - Simplified CO₂ dissipation model.
- From the software perspective, identical to the full system, ensuring portability of code.

8. User Guide
- System startup procedure
- Operating the system via the local UI
- Remote operation through ThingSpeak
- Safety considerations (CO₂ valve usage, thresholds)
9. Technical Documentation
- Class diagrams
- Task and flow diagrams
- Module descriptions
- Implementation principles

11. References
- Official datasheets of sensors and actuators
- FreeRTOS project template (GitLab link)
- ThingSpeak documentation

4.